## Slide 1
Hydrogen and the net-zero energy economy
John Perona
Metro Climate Action Transportation Team
7 May 2021

## Slide 2
What is hydrogen?
How is hydrogen manufactured?
What is hydrogen used for?
How can hydrogen be integrated into
the net-zero energy economy?
(production, storage, transport)
Policies to promote blue and green hydrogen
Hydrogen and the net-zero energy economy

## Slide 3
CH4 CH3OH CH2O HCOOH CO2
Methane Methanol Formaldehyde Formic acid Carbon Dioxide
most reduced …..…………..………………….. most oxidized
highest energy …….…………..…………………. lowest energy
High energy, reduced compounds combine
with oxygen [burn]  release (useful) energy
as they are converted to low energy compounds
A Wee Bit of Chemistry
CH4 + 2O2  CO2 + 2H2O burning CH4 releases energy + CO2 + water
2H2 + O2  2H2O burning H2 releases energy + water, no CO2

## Slide 4
Properties of Hydrogen as an Energy Carrier
Very light and found as a gas at ambient conditions
Very high energy per unit of mass, but very low energy density
Can be compressed for transport and storage (but energy cost)
Health and safety concerns (unfamiliar risks)
Carries chemical energy (H2 molecule); not electrons flowing
Storage and transport as a stable chemical; stocks not flows
Chemical reactions: industry feedstock; produce other energy-rich molecules
Data from IEA

## Slide 5
Hydrogen (H2) is an indirect greenhouse gas
H2 reacts with OH. radicals; increases ozone, methane levels
Ozone and methane are both greenhouse gases
H2 can escape atmosphere, but the main sink is soils
H2 concentration ~ 0.5 ppm [methane = 1.9 ppm]
Atmospheric lifetime of H2 ~ 2 years
Global warming potential ~ 5 (100 yrs) [methane = 28]
If H2 fully replaces fossil fuels, and 1% leaks, the climate
impact is estimated at 0.5% of present CO2 emissions
RG Derwent et al., , Int. J. Hyd. Energy, 45, 9211 (2020)
Could widespread hydrogen use
cause further warming??

## Slide 7
What is hydrogen?
How is hydrogen manufactured?
What is hydrogen used for?
How can hydrogen be integrated into
the net-zero energy economy?
(production, storage, transport)
Policies to promote blue and green hydrogen
Hydrogen and the net-zero energy economy

## Slide 8
How hydrogen is produced
Resources for
the Future,
Feb 2020
In the US, most H2 is produced from natural gas by reforming (gray)
Blue hydrogen may not be fully decarbonized

## Slide 9
Global Annual Hydrogen Production ~ 120 Mt
(120 Mt = 120 million metric tons = 120 billion kg)
Credit: Global CCS Institute, Blue Hydrogen, April 2021
96.7% Gray/Brown
1.9% Byproduct
1.1% Blue (CCS)
0.3% Green
Eats up 2% of global
energy demand
Coal source dominant
in China

## Slide 10
Making Hydrogen – CO2 emissions of various pathways
22 kg CO2/kg H2 (worst case)
Natural gas
reformation
Coal gas.
Grid run
on gas
Credit: Global CCS Institute, Blue Hydrogen, April 2021
Hydrogen production generates ~2.2% of world CO2 emissions
BECCS

## Slide 11
Steam-methane reforming: 700-1000 ◦C, low pressure, catalyst
First reaction produces a CO / H2 mixture called syngas
Syngas can also be made by heating biomass
Syngas (synthesis gas!) is a feedstock for chemicals, etc
The second reaction produces more H2
Purification is needed for some end uses
Relative amounts of CO, CO2, H2 can be fine-tuned
Making hydrogen from methane

## Slide 12: Capture and geologic storage of CO2 is essential to blue hydrogen development
CO2 is scrubbed from the H2 smoke stack emissions
CO2 is injected deep underground
Works in many industries
Only at Mt scale/year now; needs 1000x scaleup
Key challenge: economics
Capture
Underground
Injection
Pipeline
Transport
Compression
A Four Step Process

## Slide 13
Hydrogen production by electrolysis
Oxidation at
anode
Reduction at
cathode
2H2O  2H2 + O2
[reverse of H2 burning]
Credit:
DOE
Generates very high purity H2
If all global H2 by electrolysis
~4Twh (~total US electricity use)
AND would use 1.3% of world’s
energy industry water demand
Three distinct technologies
exist (vary in electrode material,
membrane, need for heat)
Credit FCHEA
Credit AIChE

## Slide 14
Circular carbon economy (holy grail)
Green H2 production from renewable electricity
Direct air capture of CO2 (large energy requirement)
Syngas and fuels production by combining CO2 and H2
Recapture CO2 from burning the synthetic fuels
Biomass harvesting is not required
K2P, 2021

## Slide 15
Surplus Columbia River hydroelectricity
will be used to generate hydrogen
This is a pilot project
May produce 2 tons of green H2 per day
Electrolyzer needs 5 MW power
(Wells Dam = 840 MW capacity)
Total US H2 needs: 57,000 MW
Feel-good story

## Slide 16
Hydrogen production from seawater – bench scale only
Freshwater resources may constrain development
in water-stressed regions
Reverse osmosis (desalination) energy cost is modest
Some detailed analysis needed here
Desalination plant, Dubai – plans to convert to solar power
Credit: Popular Science

## Slide 17
Relative costs of gray vs. blue vs. green hydrogen
Credit: Resources for the Future, A Hydrogen Future,
Exploring Pathways to Decarbonization, March 9, 2021
Crucial factors for green hydrogen development: electrolyzer cost,
capacity factor for electrolysis facilities, and price of electric power

## Slide 18
Green hydrogen costs vary with
costs of renewable electricity
IEA, The Future of Hydrogen, June 2019

## Slide 20
What is hydrogen?
How is hydrogen manufactured?
What is hydrogen used for?
How can hydrogen be integrated into
the net-zero energy economy?
(production, storage, transport)
Policies to promote blue and green hydrogen
Hydrogen and the net-zero energy economy

## Slide 21
Hydrogen Use
DRI = direct reduced iron - steel production
Refining/Ammonia/Other Pure – need pure H2
Methanol/DRI/Other mixed – H2 in a mixture
Not pictured: Energy Storage; Industrial Heat; Vehicles
IEA, June 2019

## Slide 22
Credit: IEA
Breakdown of hydrogen production and use

## Slide 23
Hydrogen production in the US, 2018
Only ~1600 miles of H2 pipeline in the United States
Most H2 is used at the site of production

## Slide 24
Hydrogen is required for producing fossil fuel products
Heavier fuel oils are “cracked” at high temperature  useful lighter products
Hydrogen reacts with the fuel oils, controls breakdown and temperature

## Slide 25
Haber Process for Ammonia Production
Ammonium salts are the basis for fertilizers
Haber Process  Green Revolution  Human population growth
Credit: Chemistry LibreTexts

## Slide 26
Hydrogen Use in Steelmaking
CO from syngas
(fossil fuel)
H2 from syngas
or renewables
Iron oxides (Fe3O4, magnetite or Fe2O3, hematite)
are the forms of iron found in most mined iron ore
But reduced iron (Fe) is needed to make steel
Steelmaking also requires carbon from coking coal
(10-15% of coal mined is used for this)
Credit: Hannu Suopajarvi

## Slide 27
Industrial Heat – Key to Reducing Industry Emissions
Data from CGEP
Potential “green” alternatives for supplying industrial heat
Temperature requirements for various industries differ
Hydrogen can meet all industry requirements. But no pure H2 used today.

## Slide 28
Hydrogen for Energy Storage on the Electricity Grid
Needed to overcome intermittency of PV solar and wind power
Storage much more expensive as PV solar and wind approach 100%
Hydrogen can replace natural gas for long-term storage
Needs storage infrastructure
Ctr. for Sustainable Systems
Univ. of Michigan

## Slide 29
2021 Toyota Mirai, MSRP from $49500
Hydrogen for transportation
Onboard hydrogen makes
electricity through
fuel cell stack
Electric motor and battery
for operation and
energy storage (like EV)
Battery recaptures energy
from braking; no plug-in
1 kilogram of H2 provides 100 kilometer driving range
1 kilogram of H2 would occupy 11 cubic meters at 1 atmosphere pressure
Today’s cars carry 5 kilograms of H2 at 700 atmospheres,
in a carbon-fiber reinforced tank. 300 mile driving range.
Metal hydride or organic nanoparticle adsorbents are in development
Credit: National Academies Press

## Slide 30
Hydrogen for heavy-duty vehicles
Larger tanks  lower pressure H2 
less energy to compress the H2
AND long driving ranges
DOE has a Million Mile Fuel Cell Truck initiative working on PEM technology to maximize onboard hydrogen use
DOE also has an H2@Scale vision
Credit: DOE

## Slide 32
What is hydrogen?
How is hydrogen manufactured?
What is hydrogen used for?
How can hydrogen be integrated into
the net-zero energy economy?
(production, storage, transport)
Policies to promote blue and green hydrogen
Hydrogen and the net-zero energy economy

## Slide 33
Issues: pipelines, shipping/trucking,
conversion and reconversion, storage (tanks, geological)
Hydrogen
Supply
Chains

## Slide 34
Hydrogen safety
Hindenburg explosion, 1937
Lakehurst, NJ
62 of 97 passengers & crew survived

## Slide 35
Liquid hydrogen
Boiling Pt. = -253C
Dry Ice (solid CO2)
Sublimes at -78.5C
Liquid nitrogen
Boiling Pt. = -196C
Major hydrogen challenge
Credit: sciencenotes.org

## Slide 36
Potential storage and transport pathways for hydrogen
MCH = methylcyclohexane
Credit: International Renewable Energy Agency (IRENA)

## Slide 37
Hydrogen conversion to other carrier molecules/fuels
Conversion means loss of 45-60% of the input electrical energy
used to make the hydrogen by electrolysis
Liquid ammonia  boiling pt = -33C, well-established technology
Credit: IEA

## Slide 38
Can natural gas pipelines carry hydrogen? How much?
Widely varying tolerance of natural gas infrastructure for hydrogen blends
Embrittlement of steel pipelines is one of the issues
Credit: IEA

## Slide 39
Credit: Sandia National Labs

## Slide 40
HyBlend project
NREL together with five other national labs, 20+ industry/academic labs
Will test hydrogen compatibility of metal and polymer pipelines
Lifecycle emissions calculations of natural gas/hydrogen blends
Costs and economic opportunities
Leverages work of Hydrogen Materials Compatibility Consortium (H-Mat) [DOE]
Also: SoCal Gas and SDG&E Hydrogen Blending Demonstration Program
https://www.sempra.com/socalgas-and-sdge-announce-groundbreaking-
hydrogen-blending-demonstration-program-help-reduce

## Slide 41
Funded by AB 8, 2012
Public-private partnership to promote
hydrogen fueling infrastructure
Cumulative sales of fuel cell
cars now over 10,000 (2021)
Includes road map for fuel cell
electric buses:
California Fuel Cell Partnership
Green = open, retail
Ahead of its time??

## Slide 42
Policy: Hydrogen and the Low Carbon Fuel Standard (LCFS)
Credit: California Air Resources Board
Electricity used for hydrogen production is also eligible for credits

## Slide 43
Policies to Promote Hydrogen
National H2 roadmap and vision; quantitative emissions reduction law
Present state in US: nonexistent
Create demand: put economic value on hydrogen
Presently in US: CA, OR LCFS, state ZEV mandates, state carbon price
Mitigate investment risks (tax credit, green bank financing, PPPs)
Presently in US: 45Q CCS tax credit
R&D, pilot projects
Presently in US: DOE funding; utility gas mixture pilot programs
Harmonize standards/remove barriers
Credit: IEA

## Slide 44
Thank you!
www.fromknowledgetopower.com
https://www.linkedin.com/in/john-perona-b31542124/
perona@pdx.edu